LESSON 25

HAZARDOUS MATERIALS: RECOGNITION AND IDENTIFICATION

OUTLINE

Objectives

Introduction

Location and Occupancy

Placards, Labels, and Markings

Other Identification Systems

Containers

Senses

Chemical and Physical Properties

Lessons Learned

Key Terms

Review Questions

Endnotes

Suggested Readings

CLASS ASSIGNMENT

Prior to this lesson:	Read Firefighter's Handbook, Chapter 25, 
pages 709-756

Length:	3 hours, 35 minutes

Equipment/Supplies:	Course outline

Transparency masters--Chapter 25

PowerPoint Presentation--Chapter 25

Overhead projector, slide projector, or LCD display

OBJECTIVES*

After completing this lesson, students should be able to:

- Identify the nine hazard classes as defined by DOT. (A)

- Identify the hazards associated with each hazard class. (A)

- Identify the standard occupancies where hazardous materials may be used or stored. (A)

- Identify the standard container shapes and sizes and common products. (A)

- Identify both facility- and transportation-related markings and warning signs. (A)

- Identify the standard transportation types for highway and rail. (O)

- Explain the use of the NFPA 704 system. (A)

- Explain the use of transportation containers in identifying possible contents. (O)

- Explain the location of emergency shutoff valves on highway containers. (O)

- Explain the importance of understanding the chemical and physical properties of hazardous materials. (O)

*Instructor's note: In the Hazardous Materials section, NFPA 1001 requires that the student receive hazardous materials training at either the Awareness or Operations Level. The Hazardous Materials section will identify which objectives are Awareness (A) or Operations (O) level. If the information exceeds the Operations level, these are noted with an (O+), which is Operations plus and is not an NFPA level.

INTRODUCTION

Firefighter's Handbook, page 711

Time: 10 minutes

Key Points

- The inability to recognize the potential for chemicals to be present can place firefighters in severe danger.

- Hazardous materials incidents have killed thousands and injured countless more.

- Four basic clues to the recognition and identification of hazardous materials are:

- Location and occupancy.

- Placards, labels, and markings.

- Container types.

- The use of senses.

LOCATION AND OCCUPANCY

Firefighter's Handbook, pages 711-712

Time: 10 minutes

Key Points

- The average home has a large amount of hazardous materials that can cause enormous problems during a response.

- In rural communities, farms present unique risks due to the storage of pesticides and fertilizers.

- All of these locations and occupancies provide the potential for the storage of hazardous materials.

- Most businesses carry some type of hazardous materials, from simple household cleaners to industrial chemicals such as pool chemicals.

PLACARDS, LABELS, AND MARKINGS

Firefighter's Handbook, pages 713-723

Time: 60 minutes

Key Points

- A number of systems are used to mark hazardous materials containers, buildings, and transportation vehicles.

- The Building Officials Conference Association (BOCA) code, which has been adopted as a regulation in local communities, requires the use of the NFPA 704 marking systems.

Placards

- The most commonly seen item for identifying the location of hazardous materials is the placard.

- DOT regulates the movement of hazardous materials by air, rail, water, roadway, and pipeline according to 49 CFR 170-180.

- The DOT has established a system of nine hazard classes that use more than twenty-seven placards to identify a shipment.

- The system is designed so that materials designated by the DOT as potentially harmful are easily identified.

- The DOT has established two tables, with different guidelines that apply to each based on their hazard level.

- The most hazardous materials are required to use placards regardless of the quantity of material being carried.

- Less hazardous materials require placarding at 1,001 pounds.

- The shipper uses the hazardous materials tables (49 CFR 107.101) to determine which labels and placards are required.

- The DOT also requires the addition of a four-digit number, known as the United Nations/North America (UN/NA) identification number, either on a placard or on an adjacent orange strip.

- This identifies a bulk shipment of over 119 gallons and provides an identity to the material.

- The nine hazard classes and sub-divisions are shown below:

- Class 1, Explosives:

- Division 1.1--Most explosive hazards.

- Division 1.2--Projectile hazards.

- Division 1.3--Fire hazards or minor blast hazards.

- Division 1.4--Minor explosion hazards.

- Division 1.5--Very insensitive explosives.

- Division 1.6--Very insensitive explosives that do not have mass explosion potential.

- Making a tactical decision to attack a fire involving explosives can endanger responders.

- Class 2, Gases:

- Division 2.1--Flammable gases that are ignitable at 14.7 psi in a mixture of thirteen percent or less in air, or has a flammable range with air of at least twelve percent.

- Division 2.2--Nonflammable, nonpoisonous, compressed gas, including liquefied gas, pressurized cryogenic gas, and compressed gas in solution.

- Division 2.3--Poisonous gases that are known to be toxic to humans and would pose a threat during transportation.

- The hazard zones associated with this division are:

- Hazard Zone A

- Hazard Zone B

- Hazard Zone C

- Hazard Zone D

- Class 3, Flammable Liquids:

- Flammable liquids have a flash point of less than 141°F.

- Combustible liquids are those with flash points above 100°F and below 200°F.

- Class 4, Flammable Solids:

- Division 4.1--Includes wetted explosives, self-reactive materials, and readily combustible solids.

- Division 4.2--Comprised of spontaneously combustible materials including pyrophoric materials or self-heating materials.

- Division 4.3--Dangerous-when-wet materials are those that when in contact with water can ignite or give off flammable or toxic by-products.

- Class 5, Oxidizers and Organic Peroxides:

- Division 5.1--The class assigned to materials that have the ability to produce oxygen, which in turn increases the chance of fire, and during fires makes the fire burn more intensely.

- Division 5.2--The organic peroxides, which have the ability to explode or polymerize, and if contained is an explosive reaction. These are divided into seven types:

- Type A

- Type B

- Type C

- Type D

- Type E

- Type F

- Type G

- Class 6, Poisonous Materials:

- Division 6.1--Materials that are so toxic to humans that they would present a risk during transportation.

- Division 6.2--Comprised of microorganisms or their toxins, which can cause disease to humans or animals.

- Hazardous zones A and B are associated with Class 6 materials.

- Class 7, Radioactive Materials

- Those materials determined to have radioactive activity at certain levels.

- Although there is only one placard, the labels are further subdivided into Radioactive I, II, and III, with Level III being the greatest hazard.

- Class 8, Corrosives:

- Includes both acids and bases, and is described by the DOT as a material capable of causing visible destruction in skin or corrodes steel or aluminum.

- Class 9, Miscellaneous Hazardous Materials:

- A general grouping that is comprised of mostly hazardous waste:

- This is known as a catch-all category.

- Other placards and labels:

- The Dangerous placards are used when the shipper is sending a mixed load of hazardous materials.

- Specific name placards are sometimes used instead of a generic class placard.

- The Stow Away from Foodstuff placards indicate that a poisonous material is being transported, but it is not poisonous enough to meet the requirements to be placarded as a poison.

- "Other Regulated Material--Class D" (ORM-D) is a classification that is left over from a previous DOT regulation.

- "Marine Pollutant" is displayed on shipments that, if released into a waterway, would damage the marine life.

- Elevated temperature material will have a "HOT" label either to the side of, or on the placard, if it meets the following criteria:

- A liquid above 212°F.

- A liquid that is intentionally heated and has a flash point above 100°F.

- A solid at 464°F or above.

- "Infectious Substances" is a label that is sometimes used on the outside of trucks.

- The Fumigated placard is used when a trailer or railcar has been fumigated with a poisonous material.

- The Residue placard is used in rail transportation and identifies the last product the tank held.

- A white square background is used to identify the following shipments while on rail: explosives 1.1 or 1.2, poison gas, or poison gas residue.

- Placards are only required for shipments that exceed 1,001 pounds, except for certain materials.

- It is suspected that ten to twenty percent of the trucks traveling the highway are not placarded at all or placarded incorrectly.

- The fact that an incident involves a truck or train should immediately alert the first responder to the potential for the presence of hazardous materials, and when a placard is involved extra precautions should be taken.

Labels

- Package markings must include the shipping name of the material, the UN/NA identification number, and the shipping and receiving companies' names and addresses.

- Materials that pose inhalation hazards must affix an Inhalation Hazard label next to the shipping name.

- Hazardous wastes will be marked "Waste" or will use the EPA labeling system to identify these packages.

- The primary label will have the class and division number in the bottom triangle, while the subsidiary label will not have the number.

OTHER IDENTIFICATION SYSTEMS

Firefighter's Handbook, pages 723-727

Time: 20 minutes

Key Points

NFPA 704 System

- One of the more common systems used to identify the presence of hazardous materials is the NFPA 704 system.

- The system is much like the placarding system and relies on a triangular sign that is divided into four areas.

- The four areas are divided by color as well, and use a ranking system to identify severity:

- Health hazard--blue.

- Fire hazard--red.

- Reactivity hazard--yellow.

- Special hazard--white.

- This system uses a ranking of 0-4 with a ranking of 0 presenting no risk and a ranking of 4 indicating severe risk.

Hazardous Materials Information System

- Referred to as the HMIS, the system was designed to provide a mechanism to comply with the federal hazard communications regulation.

- This regulation requires that all containers be marked with the appropriate hazard warning and that the ingredients be provided on the label.

- Most systems are similar to the NFPA 704 system and use blue, red, and yellow colors with a numbering system that provides an identification hazard.

- The chart is usually stored with the MSDSs.

- Each HMIS is different, and responders should not assume any particular hazard level until the warning levels can be determined.

Military Warning System

- The military uses the DOT placarding system whenever possible, but in some cases they may use their own system.

- The higher the hazard, the more likely there will be an escort for the shipment.

- The phone numbers to contact the military are in the DOT North American Emergency Response Guidebook (NAERG) book, along with Chemtrec's and other emergency contact numbers.

- The military typically uses its own marking system to mark the buildings at their facilities.

Pipeline Markings

- Any place where an underground pipeline crosses a mode of transportation, the owner is required to place a sign that indicates the pipeline contents, owner, and emergency contact numbers.

- An incident involving a pipeline can be a serious event.

- Within the fire department alone, considerable resources may be required such as command staff, logistic support, communications, and tactical units.

- The product in the pipelines varies from liquefied gases and petroleum products to slurred material.

Container Markings

- Most containers, such as drums, are marked with the contents of the drum.

- In bulk shipments, the DOT requires that some products have their own placard, such as the Chlorine placard.

Pesticide Container Markings

- Due to their toxicity, pesticides are regulated by the EPA as to how they are to be marked.

- In addition to the pesticide's manufacturer name, the label will also contain a signal word such as "Danger," " Warning," or "Caution."

- In the United States, the EPA requires an EPA registration number, while in Canada the label will have a pest control number.

CONTAINERS

Firefighter's Handbook, pages 727-747

Time: 45 minutes

Key Points

- Hazardous materials come in a variety of containers in many shapes and sizes, from one-ounce bottles and larger bags to tanks and ships carrying hundreds of thousands of gallons.

- Homes contain a wide variety of storage containers. Compressed gas cylinders hold propane, steel containers hold flammable and combustible liquids, and bottles, jars, and small drums hold other various products.

- The type of materials contained within and the final use for the product, determines the packaging.

- The type of container usually provides a good clue as to the contents of the package.

- When looking at the recognition and identification process, the first responder should be alert for anything unusual when arriving at an incident.

General

- With the popularity of shipping clubs and discount warehouses, more and more homeowners are buying materials by the case, when, in the past, they bought in much smaller quantities.

- Materials being transported to suppliers may be transported in larger cardboard boxes and then broken down for the retail level.

- From 1-ounce bottles to 1-gallon bottles, the variety of containers is endless and the types of products contained in them are too numerous to mention.

- Carboys provide a cover to protect materials against potential damage during transportation. Therefore, if the container is dropped, the bottle inside should survive the fall.

- While ensuring the material's compatibility with the container it will be stored in is important, the one area that usually results in a release is the use of an improper cap.

- Bags are commonly used as containers for chemicals.

- Bags carry anything from food items to poisonous pesticides, and the method of transportation varies widely.

- Cylinders vary from 1-pound sizes up to several thousand pounds and carry a variety of chemical products.

- The pressures range from a low of 200 psi to a high of 5,000 psi.

- Specialized cylinders that hold cryogenic gases appear to be high pressure, but in reality they are low pressure.

- Cylinders usually have relief valves or frangible disks in the event that they are overpressurized or are involved in a fire.

- Both totes and bulk tanks are becoming more common, since their size varies between drums and tank trucks, and are used for a variety of purposes.

- They are constructed of steel, aluminum, stainless steel, lined materials, poly tanks, and other products.

- A common incident with totes can occur during offloading, when the swinging valve can be knocked off.

- One unusual tote is made to transport calcium carbide, a material that forms acetylene gas when it gets wet, which is reactive and very flammable.

Pipelines

- Pipelines vary in size and pressure, but normally are sized between 
1/2 inch and more than 6 feet.

- Pipelines can originate from any bulk storage facility and can cross many states. Some type of pipeline system is found in every state.

Highway Transportation Containers

- The type of vehicle provides some important clues as to the possible contents of the vehicle.

- There are four basic tank truck types that carry hazardous materials, with some additional specialized containers. These four types are the:

- DOT-406/MC-306 gasoline tank truck.

- DOT-407/MC-307 chemical hauler.

- DOT-412/MC-312 corrosive tanker.

- MC-331 pressurized tanker.

- Tractor-trailers carry a whole variety of hazardous materials and portable containers.

- Leakage is often found in containers known as intermodal containers or, more commonly, sea containers.

- Tank trucks can carry anywhere from several hundred gallons to up to a maximum of 10,000 gallons.

- The most common tank truck is the gasoline tank truck, which usually carries 5,000 to 10,000 gallons.

- The DOT allows trucks that were manufactured before the new regulation to remain on the road, as long at they meet the applicable inspection requirements.

- The most common tank truck on the road today is the DOT-406/MC-306.

- Along with making a large number of shipments, these tank trucks suffer the most accidents.

- The DOT-407/MC-307 tankers are the workhorses of the chemical industry.

- These tanks usually hold between 2,000 to 7,000 gallons, lower amounts than the 406/306 because most of the products they carry are heavier than petroleum products.

- The uninsulated tank is round and has stiffening rings around the tank.

- The insulated tank is a covered version of the uninsulated tank, although in some cases it has a slightly smaller inner tank.

- The DOT-412/MC-312 tankers carry a wide variety of corrosives, both acids and bases.

- These tankers are constructed of a single tank that carries up to 7,000 gallons.

- MC-331 tanks look like bullets and are noted for their rounded ends and smooth exteriors.

- They carry gases that are liquefied by pressure.

- The tanks contain a liquid along with a certain amount of vapor.

- The pressure in these tanks is of a primary concern when firefighters are responding to incidents involving these tanks.

- MC-338 cryogenic tankers are uniquely constructed tanks with an outer shell.

- The inner container is steel or nickel, with a substantial layer of insulation. The exterior is made of aluminum or mild steel.

- Tube trailers contain several pressurized vessels, constructed much like the MC-331 tank.

- They are constructed of steel and have pressures ranging from 2,000 to 6,000 psi.

- The piping and controls are usually located on the rear of the trailer, but could be in the front.

- Dry bulk tanks resemble large uninsulated MC-307s in shape, with bottom hoppers to unload the product.

- The tanks hold dry products and sometimes a slurry, like concrete.

- The potential hazard when dealing with these tankers is predominantly environmental, but at times these tankers contain toxic materials.

- Hot materials tankers vary in that they can be modified MC-306s, 307s, or dry bulk containers.

- They may have a mechanism within to keep the material hot or it may be loaded hot.

- If the material is allowed to cool, it can cause problems for the responders or the shipping company.

- Intermodal tanks are increasing in use and carry the same types of products as their highway and rail companions.

- They are called intermodal (IM) because they can be used on ships, railways, or highways.

- Intermodals follow three basic types: nonpressurized, pressurized, and highly pressurized.

- The piping for the IM-102 is contained outside of the tank, usually on the ends, with a manhole on top of the tanks.

Rail Transportation

- As with highway transportation, there are only a few types of railcars, and they are similar to their highway counterparts.

- Rail incidents usually involve multiple railcars, whereas highway incidents usually involve one or two trucks.

- Railcars come in three basic types: nonpressurized, pressurized, and specialized cars.

- They carry chemicals, combustible and flammable liquids, corrosives, and slurries.

- Corrosive cars will be smaller than the other nonpressurized cars, but will have the characteristics of other nonpressurized cars, and will have the characteristic strip of protective coating around the middle.

- Pressurized tank cars also carry a wide variety of products, including flammable and poisonous gases.

- Specialized railcars have the same characteristics as highway vehicles, and, in some cases, highway box trailers are loaded onto flatbed railcars.

- Much like highway trailers, there are freight boxcars that haul the same products as their highway trailers, with the exception of carrying much larger quantities.

- Dry bulk closed railcars are common, and open hopper cars are also found.

- Cryogenics are also carried in railcars and maintain the same low pressure as in highway transportation, using the characteristic venting when the pressure increases.

- Railroads use the same placarding system used on highways, with certain exceptions.

- In addition to a placard, the name of the hazardous material is stenciled on two sides of the car.

- Bulk storage tanks store a variety of products and range in size from 
250 gallons up to millions of gallons.

- In residential homes, the most common tank is a 250-gallon home heating oil tank, and some homes or small businesses may also have gasoline or diesel fuel tanks.

- The two basic groupings of tanks are: in-ground and aboveground.

- A substantial release from a million-gallon tank of gasoline that escapes a facility would require an enormous response from the emergency responders.

- Underground tanks are usually constructed of steel and are coated with an anticorrosion material.

- The loading piping is located separately and all of the fill pipes are located in the same area for easy transfer from a tank truck.

- Most gas station tanks are 10,000 to 25,000 gallons in size and, if not properly monitored, can slowly release a substantial amount of product over a short period of time.

- Another common problem arises when farms are redeveloped into housing developments.

- The tank and environmental industry refers to a leaking underground storage tank as a LUST.

- Aboveground tanks are becoming more and more common, although they have been used in some capacities for many years.

- The containment area must be able to hold the contents of the largest tank within the containment.

- Depending on the weather conditions, the containment area's gate valve may be left in an open position.

- Upright storage tanks come in three basic construction types: ordinary tank, external floating roof tank, and internal floating roof tank.

- Some ordinary tanks are purposely constructed without a roof in place.

- External floating roof tanks are used to eliminate the buildup of vapors.

- External floaters can be seen from the top of the tanks, and a ladder is 
affixed to the roof to allow access.

- Internal floaters have an additional roof over the top of the tank.

- Specialized tanks are a combination of the tank types and include pressurized tanks and cryogenic tanks.

- Common high-pressure commodities are liquefied propane, liquefied natural gas, and other gaseous or liquefied petroleum gases.

- Upright cryogenic storage tanks are located in almost every community.

- Most hospitals are supplied with liquid oxygen (LOX) through a cryogenic tank.

SENSES

Firefighter's Handbook, pages 747-748

Time: 10 minutes

Key Points

- The use of vision and hearing are acceptable senses that could be vital while investigating for potential chemical releases.

- Sensory clues gained from other people are useful to help identify the spilled material.

- Many toxic materials can be harmful if touched because the material can be absorbed through the skin.

CHEMICAL AND PHYSICAL PROPERTIES

Firefighter's Handbook, pages 745-754

Time: 45 minutes

Key Points

- The chemical and physical properties outlined here are for a firefighter's level of response.

States of Matter

- The basic chemical and physical properties that are important to understand are the three states of matter: solid, liquid, and gas.

- The control methodology for each state increases in difficulty, with a solid being controlled simply while a gas would be more difficult.

- The means for chemicals hurting someone also varies with the state of material.

- Adjoining issues relating to the states of matter are melting point, freezing point, boiling point, and condensation point.

- All of these are related because they are the points at which a material changes its state.

- The melting point is the temperature at which a solid must be heated to transform into the liquid state.

- The freezing point is the temperature when a liquid is transformed into a solid.

- The boiling point is reached when the liquid is heated to the point at which evaporation takes place.

- The important thing to remember about boiling points is that when the liquid approaches this temperature, vapors are being produced that can cause problems.

Vapor Pressures

- Out of all the chemical and physical properties displayed by hazardous materials, vapor pressure is one of the most important to a hazardous materials responder.

- Vapor pressure has to do with the amount of vapor released from a liquid or a solid.

- The true definition is the pressure that is exerted on a closed container by the vapors coming from the liquid or solid.

- The ability of a material to go from a solid to a gas is called sublimation.

- Vapor pressures are measured in three ways: millimeters of mercury (mm Hg), pounds per square inch (psi), and atmospheres (atm).

- Chemicals with a vapor pressure above 40 mm Hg can be considered inhalation hazards in addition to any other route of exposure they may possess.

Vapor Density

- It is easy to confuse vapor pressure with vapor density, but they have two entirely different meanings.

- Vapor pressure determines whether the vapors will rise or fall.

- Air is given a value of one, after which all other gases are compared to air.

- Gases that have a vapor density of less than one will rise in air and will dissipate, while gases with a vapor density greater than one will stay low to the ground.

Specific Gravity

- This chemical property is similar to vapor density in that it determines whether a material sinks or floats in water.

- Specific gravity is of primary concern when efforts are being taken to limit the spread of a spill through the use of booms or absorbent material.

- Water is given a value of one, and chemicals that have a specific gravity of less than one will float on water.

- Also of concern are materials that are water soluble, that have the ability to mix with water, rather than sink or float.

Corrosivity

- Corrosivity is a term that is applied to both acids and bases, and is used to describe a material that has the potential to corrode or eat away the skin or metal.

Chemical Reactivity

- Chemicals, when they mix, will have one of three types of reactions: exothermic, endothermic, or no reaction.

- The most common is the exothermic reaction, which results in the release of heat.

- An endothermic reaction is one in which the heat generated by the reaction is absorbed, and no heat is released.

Flash Point

- A flash point is described as the temperature of a liquid at which, when heated by an ignition source, a flash fire occurs.

- Following closely behind the flash point is the fire point of a liquid.

Autoignition Temperature

- The autoignition temperature is the temperature at which a material will ignite on its own without an ignition source. This is also referred to as the ignition temperature.

- Depending on the context, the term self-accelerating decomposition temperature (SADT), may be used in place of the autoignition temperature.

- The two main areas within a flammable range are the lower explosive limit and the upper explosive limit.

- The lower explosive (flammable) limit (LEL) is the lowest amount of vapor mixed with air that can provide the proper mixture for a fire or explosion.

- The upper explosive (flammable) limit (UEL) is the highest amount of vapor mixed with air that will sustain a fire or explosion.

- Ventilation should be carried out using non-spark-inducing devices, and great care should be taken to minimize any potential electrical arcs, such as not using light switches or doorbells.

- Toxic products of combustion are an area where firefighters can suffer considerable chemical exposures.

- The worst chemical accident a firefighter can respond to is a house, car, or dumpster fire.

- Even burning wool or hay produces extremely toxic gases.

- Due to this constant exposure to these and other materials, it is important for firefighters to wear all of their protective clothing, especially the SCBA.

WRAP-UP

Time: 15 minutes

Key Points

- The ability to recognize and identify the potential for hazardous materials to be present at an incident is important for the first responders.

- At any incident there is always a factor that relates to the recognition and identification process.

- It is important for firefighters to remember that they do not have to memorize everything, but do have to know where to access any information that they might need.

- Each fire department should have a contact person available around the clock to obtain any needed resources.

- Physical properties of chemicals will greatly affect how a hazardous material may react and also how it should be managed.

- Firefighters must be able to use available resources and remember to elicit their help early on in an incident.

Assignment

- Read Chapter 26 in Firefighter's Handbook, pages 757-780

- Optional: Complete Firefighter's Handbook Workbook, Chapter 26

Instructor Preparation

PowerPoint Presentation--Chapter 26

Transparency masters--Chapter 26

Overhead projector, slide projector, or LCD display

HAZMAT placards, ERG book, and MSDS samples